Vivarium Electronics Model VE-300X2

Thank you for selecting Vivarium Electronics to meet your thermostat control needs.  The Model VE-300X2 Dual Zone thermostat has several advanced features including a full featured display, alarms, built in night drop and more.  All of these features are available on both zones.  Please see the product specifications at the end of this document for full feature list.

Installation:

- Your new VE-300X2 thermostat includes the VE-300X2 unit, two (2) 10 foot replaceable temperature probe and a 6 foot power cord.

- Install the temperature probes in the RJ-11 jacks on the rear panel of the thermostat.  Use the jack labeled “#1” for AC Output Zone 1 and the jack labeled “#2” for AC Output Zone 2.

- The included power cord will need to be plugged into the rear panel as well.  Plug the power cord into any standard, grounded wall power outlet.

- Plug your heater(s) into the AC Out grounded receptacle.  You will want to be sure that your probe #1 is monitoring the heat source plugged into “Zone 1” and the same for Zone 2.  You may use an outlet strip/Surge Protector for convenience.  Your total heater wattage cannot exceed 900 Watts.

combined.  If you are only planning on using one zone then you will use both the probe jack and AC Output for Zone 1.  You will also want to set the number of zones in the user menu to 1.  See below for further information on programming.

- Indoor Use Only

Once your VE-300X2 has been installed you will see a short startup screen before moving to the default display.  The display will show the current time (flashing if it has not been set), the current Set Point and the current probe temperature for Zone 1.  At this time only Zone 1 is activated in the programming.  See below.

Warning:  Fire, electrical shock and unit failure can result from improper installation and misuse.

Menu Options:

You can now program your VE-300X2 by depressing the “Enter/Menu” button. Be sure to save your new settings by depressing the “Enter/Menu” button.  The VE-300X2 will confirm the new setting by displaying “Entry Accepted”.  If you do not then your changes will not be saved!

Once you have entered the menu you can navigate through your choices using the +/- keys.  You will have the following options:

- Set Daytime Temperature- Use the +/- keys to select your desired temperature setting.  If only one zone is activated you will not be allowed to access the set point for Zone 2.

- Night Drop Amount- Use the +/- keys to select the number of degrees you want your temperature to drop at the start of the night temperature period.  Example- If your Daytime Temperature setting is 80°F and you wish to drop to 70°F at night you would enter a value of “10°F”.  If you DO NOT wish to have a night temperature drop then use a value of “0°F”.  If only one zone is activated you will not be allowed to access the Night Drop for Zone 2.

- Set Start of Daytime Temp- Here you set the time of day you want to switch from the Night Drop Setting (if used) to the Daytime Temperature.  If you have a value of “0°F” in the Night Drop Amount this setting will be ignored.  This time setting must be during AM hours.  If only one zone is activated you will not be allowed to access the settings for Zone 2.

- Set Start of Night Temp- Here you set the time of day you wish to switch to your Night Drop Setting.  If you have a value of “0°F” in the Night Drop Amount this setting will be ignored.  This time setting must be during PM hours.  If only one zone is activated you will not be allowed to access the settings for Zone 2.

- Set Time of Day- Set the current time.  This will display the correct time on the default display and also act as the clock for your day and night temperature cycle if being used.  Time is kept in the event of a power failure.  If the time of day is lost with a power failure the battery will require replacement.  The VE-300 uses a 2032 coin cell.  Always unplug the thermostat before opening the case to replace the battery

- Select Heater Mode- If only one zone is activated you will not be allowed to access the heater mode for Zone 2.

  - ON/OFF operation you will be prompted to enter a Hysterisis value.  This is the number of degrees below the Daytime Temperature setting the thermostat will turn power back on.  Example- If your Daytime Temperature is 80°F and the Hysterisis is 3 the VE-300X2 will turn OFF upon reaching 80°F and ON when the temperature drops down to 77°F.  This setting will increase or decrease the number of times per hour the VE-300X2 will switch on and off.  The smaller the Hysterisis value the more tightly the temperature will be controlled.

  - Proportional Mode- This mode will use short pulses of power to your heater to control the heat output.  By gradually increasing or decreasing the amount of power to the heater the VE-300X2 is able to maintain very accurate temperature settings.  In most applications this is the preferred mode of operation.

- Disable/Enable Alarms- This will allow you to disable the Temp Overshoot Alarm as well as the Too Long to Setpoint alarm.  Please see the specifications at the end of this document for the alarm thresholds.  All probe alarms will remain active to protect against probe failure, damage or removal at all times.  Vivarium Electronics recommends you have the alarms feature active at all times!  If only one zone is activated you will not be allowed to access the alarm settings for Zone 2.

- Set Number of Zones- The factory default setting is one zone.  If you wish to use both zones on your VE-300X2 you will need to set this menu option to “2”.  Once the number of zones has been set to “2” you will be able to access all of the Zone 2 settings in the remaining menu items.  You will also be able to access the Hi/Lo History values for Zone 2 on the default screen.  IMPORTANT- If you are only using a single zone currently we recommend using Zone 1 and setting this menu item to “1”.  If you do not have the Zone 2 probe actively controlling a heater you will have alarms sound on this zone unless Zone 2 is disabled.

VE-300X2 Features:

- History- The VE-300X2 will also store the Hi and Lo temperatures for both zones during operation.  You can toggle the default display to view these recorded temperatures by depressing the “history” button.  You can reset the Lo or Hi history value by depressing the “clear” button while the value is displayed.  If only Zone 1 is currently active you will not be able to access history for Zone 2.  You can also view the set point values for both zones with this feature.  These values will be saved by the battery backup in case of power failure.  If they are not, the battery needs replacement. The VE-300 uses a 2032 coin cell.  Always unplug the thermostat before opening the case to replace the battery.

- Power output- The green indicator light on the front panel shows the power output level.  A steady off display indicates no power output.  A steady on displays a full power to the heater.  If flashing the rate of flash indicates the level of power being applied to the heater.  The upper LED indicates power output for Zone 1 and the lower LED Zone 2.

- Alarms- The VE-300X2 has several alarm functions.  Each zone can be independently enabled or disabled in the programming.

The Sensor Failure alarm can not be disabled by the user.  This alarm constantly monitors the output of the digital probe to ensure that the signal the thermostat is receiving is not corrupted.  Should the probe cord be severed, the probe unplugged or the sensor fail the VE-300X2 will immediately turn off the heater output, flash an error message on the display and sound the buzzer.  This will continue until the fault is corrected.

The Temperature Overshoot alarm will occur when the actual probe temperature exceeds the set point by 4 or more degrees.  The alarm can be temporarily silenced by depressing the “enter” key.  The alarm will automatically reset itself once the fault has been corrected.  An example of this would be the overshoot sometimes seen with an aggressive heater during initial setup.  Once the heater stabilizes the fault will correct itself and operation will continue normally.  This alarm can be disabled by the user in the menu.  With the alarm disabled the VE-300X2 will continue to operate normally and power to the heater will be shut off any time it exceeds the Setpoint but no alarm message will be shown and the buzzer will not sound.

The Too Long to Setpoint alarm will occur any time the Setpoint has not been reached for more than 30 minutes.  This can be temporarily silenced with the “enter” key and will reset automatically or it can be deactivated in the Alarms menu.  This alarm will warn the user if the heater has failed or if the probe has become dislodged from the cage.  Any time this alarm is activated power to the heater will be shut off.

Each zone has independent alarms.  Any alarms will display the zone where the alarm occurred.  If Zone 2 is not being used, to avoid false alarms we recommend disabling Zone 2 in the “Set Number of Zones” menu option.

IMPORTANT:

It is very important that you inspect your thermostat sensor probe location and the integrity of 	your heat source on a regular basis.  If using under tank/tub heating it is especially important you 	check the element on a regular basis and ensure that it is not above 105° F actual temperature 	under the enclosure or an unsafe condition can arise.  Heat can become trapped in these areas and 	unless monitored can cause element failure.

Questions or Comments?-

You can contact Vivarium Electronics for support, general questions and other inquiries at sales@reptilebasics.com

Visit the VE website for further information and to find a reseller near you at www.vivariumelectronics.com

Vivarium Electronics is a division of Reptile Basics Inc.

Specifications:

900 Watt maximum load- both zones combined.  For example, if Zone 1 currently has a load of 400 watts that will allow a maximum of 500 watts to be used on Zone 2.

Fuse- 5mmx20mm glass fast acting 8 Amp

Overshoot Alarm Threshold- 4° F

Too Long to Setpoint Alarm- 30 minutes

Operating Range- 25°F to 140°F

Night Drop-  30°F Maximum

Replacement Battery- CR2032 Coin Cell

Limited Warranty:

Vivarium Electronics warrants all components and workmanship of this unit for a period of one year from original date of purchase and a maximum of two years from date of manufacture. Vivarium Electronics makes no warranty expressed or implied, other than that stated herein. Vivarium Electronics warranty of merchantability or any other warranty, including this limited warranty, shall be limited solely and exclusively to the repair or replacement of a defective product. Vivarium Electronics will in no event be liable for any special, incidental or consequential damages. This warranty does not include failure caused by accident, misuse, any damage from any source or connection to faulty or inappropriate electrical source.

This warranty shall be voided in the event the product is altered or tampered with in any way or used for any purpose other than that for which it is intended

V2.0